## Slide 1: IP and Networking Basics
Selection of slides taken from Internet Society Workshop Resource Centre:
http://ws.edu.isoc.org/data/2010/15678359774b67528c8924a/lecture-01-mon-tue-addressing-ios.pdf

## Slide 2: A small internetwork or (small “i”) “internet”

## Slide 3: The principle of “Internetworking”
We have lots of little networks
Many different owners/operators
Many different types
  Ethernet, dedicated leased lines, dialup, optical, broadband, wireless, ...
Each type has its own idea of low level addressing and protocols
We want to connect them all together and provide a unified view of the whole lot (treat the collection of networks as a single large internetwork)‏

## Slide 4: What’s the Internet: “nuts and bolts” view
millions of connected computing devices: hosts, end-systems
  PC’s workstations, servers
  PDA’s phones, toasters
  running network apps
communication links
  fiber, copper, radio, satellite
routers: forward packets (chunks) of data through network
local ISP
company
network
regional ISP
router
workstation
server
mobile

## Slide 5: What’s the Internet: “nuts and bolts” view
local ISP
company
network
regional ISP
router
workstation
server
mobile
protocols: control sending, receiving of messages
  e.g., TCP, IP, HTTP, FTP, PPP
Internet: “network of networks”
  loosely hierarchical
  public Internet versus private intranet
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force

## Slide 6: What’s the Internet: a service view
local ISP
company
network
regional ISP
router
workstation
server
mobile
communication infrastructure enables distributed applications:
  WWW, email, games, e-commerce, database, e-voting, more?
communication services provided:
  connectionless
  connection-oriented

## Slide 7: The OSI Model
Upper Layers
Application oriented
“End-to-End”-Layers
Lower Layers
Network oriented
“Hop-by-hop” layers
1
3
2
4
5
6
7
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 8: Why layering?
Dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure does not affect rest of system

## Slide 9: The IP Hourglass Model
Network layer
PPP
ATM
Optics
ADSL
Satellite
3G
Ethernet
IP
UDP
TCP
HTTP
FTP
Telnet
DNS
SMTP
Audio
Video
RTP
Physical and Data link layer
Application layer
Transport layer

## Slide 10: Layer Interaction: TCP/IP Model
Host
Router
Host
Application
TCP or UDP
IP
Link
Physical
IP
Link
Link
IP
Link
Link
Application
TCP or UDP
IP
Link
Physical
Physical
Hop by hop
End to end
Router

## Slide 11: End-to-end layers
Upper layers are “end-to-end”
Applications at the two ends behave as if they can talk directly to each other
They do not concern themselves with the details of what happens in between

## Slide 12: Hop-by-hop layers
At the lower layers, devices share access to the same physical medium
Devices communicate directly with each other
The network layer (IP) has some knowledge of how many small networks are interconnected to make a large internet
Information moves one hop at a time, getting closer to the destination at each hop

## Slide 13: Layer Interaction: TCP/IP Model
Host
Router
Host
Application
TCP or UDP
IP
Link
Physical
IP
Link
Link
IP
Link
Link
Application
TCP or UDP
IP
Link
Physical
Physical
Router

## Slide 14: Layer Interaction: The Application Layer
Host
Router
Host
Application
TCP or UDP
IP
Link
Physical
IP
Link
Link
IP
Link
Link
Application
TCP or UDP
IP
Link
Physical
Physical
Router
Applications behave as if they can talk to each other, but in reality the application at each side talks to the TCP or UDP service below it.
The application layer doesn't care about what happens at the lower layers, provided the transport layer carries the application's data safely from end to end.

## Slide 15: Layer Interaction: The Transport Layer
Host
Router
Host
Application
TCP or UDP
IP
Link
Physical
IP
Link
Link
IP
Link
Link
Application
TCP or UDP
IP
Link
Physical
Physical
Router
The transport layer instances at the two ends act as if they are talking to each other, but in reality they are each talking to the IP layer below it. The transport layer doesn't care about what the application layer is doing above it.
The transport layer doesn't care what happens in the IP layer or below, as long as the IP layer can move datagrams from one side to the other.

## Slide 16: Layer Interaction: The Network Layer (IP)
Host
Host
Application
TCP or UDP
IP
Link
Physical
IP
Link
Link
IP
Link
Link
Application
TCP or UDP
IP
Link
Physical
Physical
Router
The IP layer works forwards messages hop by hop from one side to the other side.
The IP layer has to know a lot about the topology of the network (which host is connected to which router, which routers are connected to each other), but it doesn't care about what happens at the upper layers.
Router

## Slide 17: Layer Interaction: Link and Physical Layers
Host
Router
Host
Application
TCP or UDP
IP
Link
Physical
IP
Link
Link
IP
Link
Link
Application
TCP or UDP
IP
Link
Physical
Physical
Router
The link layer doesn't care what happens above it, but it is very closely tied to the physical layer below it.
All links are independent of each other, and have no way of communicating with each other.

## Slide 18: Layering: physical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data

## Slide 19: Frame, Datagram, Segment, Packet
Different names for packets at different layers
  Ethernet (link layer) frame
  IP (network layer) datagram
  TCP (transport layer) segment
Terminology is not strictly followed
  we often just use the term “packet” at any layer

## Slide 20: Encapsulation & Decapsulation
Lower layers add headers (and sometimes trailers) to data from higher layers
Application
Transport
Network
Data Link
Data Link
Network
Data
Transport Layer Data
Header
Network Layer Data
Header
Data
Header
Header
Link Layer Data
Data
Header
Header
Header
Header
Trailer
Trailer

## Slide 21: Layer 2 - Ethernet frame
Destination and source are 48-bit MAC addresses (e.g., 00:26:4a:18:f6:aa)
Type 0x0800 means that the “data” portion of the Ethernet frame contains an IPv4 datagram. Type 0x0806 for ARP. Type 0x86DD for IPv6.
“Data” part of layer 2 frame contains a layer 3 datagram.
Preamble
Dest
6 bytes
Source
6 bytes
Data
46 to 1500 bytes
CRC
4 bytes
Type
2 bytes

## Slide 22: Layer 3 - IPv4 datagram
IHL
Differentiated Services
Total Length
Version
Fragment Offset
Identification
Flags
Time to Live
Protocol
Header Checksum
Source Address (32-bit IPv4 address)‏
Destination Address (32-bit IPv4 address)‏
Data (contains layer 4 segment)‏
Padding
Options
Protocol = 6 means data portion contains a TCP segment. Protocol = 17 means UDP.
Version = 4 If no options, IHL = 5 Source and Destination are 32-bit IPv4 addresses

## Slide 23: Basic Structure of an IPv4 Address
133
27
162
125
10000101
00011011
10100010
01111101
85
1B
A2
7D
32 bit number (4 octet number): (e.g. 133.27.162.125)‏
Decimal Representation:
Binary Representation:
Hexadecimal Representation:

## Slide 24: Layer 4 - TCP segment
Source and Destination are 16-bit TCP port numbers (IP addresses are implied by the IP header)‏
If no options, Data Offset = 5 (which means 20 octets)‏
Source Port
Destination Port
Sequence Number
Acknowledgement Number
Data Offset
Window
Reserved
ACK
URG
EOL
RST
SYN
FIN
Checksum
Urgent Pointer
Data (contains application data)‏
Padding
Options

## Slide 25: The need for Packet Forwarding
Many small networks can be interconnected to make a larger internetwork
A device on one network cannot send a packet directly to a device on another network
The packet has to be forwarded from one network to another, through intermediate nodes, until it reaches its destination
The intermediate nodes are called “routers”

## Slide 26: Hop by Hop Forwarding