## Slide 2: Optimising HTTP
COMP3227 Web Architecture and Hypertext Technologies
Dr Nicholas Gibbins – nmg@ecs.soton.ac.uk

## Slide 3: Physical Limits
Upper limit on speed of communication is the speed of light: c = 300,000,000 m/s
A message sent halfway round the world on a great circle route will take a minimum of 0.067 s to reach its destination
Image: NASA
~20,000 km

## Slide 4: Network Latency
The time between a source sending a packet and the destination receiving it
Actual speed of communication will be less than the speed of light:
  Optical fibre is typically ~70% of c
  Coaxial cable may be >80% of c
Routers, switches, etc introduce delays
Image: NASA
0.067s

## Slide 5: The Internet Protocol Suite
Link Layer
physical transmission
Internet Layer
addressing and routing
Transport Layer
host-to-host
Application Layer process-to-process
Transmission Control Protocol (TCP)
User Datagram Protocol (UDP)
Internet Protocol (IP)
Ethernet
802.11 (WiFi)
HTTP SMTP FTP DNS SSH IMAP POP TLS ...

## Slide 6: HTTP over TCP
HTTP runs on top of TCP (Transmission Control Protocol)
  TCP provides a reliable connection
  Guarantees that packets will eventually reach their destination
  Lost packets are resent
Opening an HTTP connection requires that a TCP connection be opened first

## Slide 7: TCP Set-up and Teardown
TCP establishes reliable connection using a three-way handshake
  SYN, SYN/ACK, ACK
Lower limit for the duration of this exchange to a host at the antipodes: 0.2 s
  for just the TCP connection (no HTTP)
  at the speed of light
  without additional delays
  before any additional overhead from the TLS handshake
SYN
SYN/ACK
ACK
0.067 s
0.067 s
0.067 s
0.2 s

## Slide 8: HTTP/1.0 and earlier
Before HTTP/1.1, each HTTP request used a separate TCP connection
Expensive and time-consuming!
  3-way handshake for each TCP open
  4-way handshake for each TCP close
  Latency issues
Some clients open multiple connections at same time
  Increased server load to handle many simultaneous connections
GET
200 OK
GET
200 OK
GET
200 OK
TCP open
TCP close
TCP open
TCP close
TCP open
TCP close

## Slide 9: HTTP keep-alive
HTTP/1.1 introduced keep-alive
TCP connections reused for multiple HTTP requests
  one TCP open and TCP close handshake
Still latency issues, but now in the application layer rather than the transport layer
GET
200 OK
GET
200 OK
GET
200 OK
TCP open
TCP close

## Slide 10: HTTP pipelining
Also available from HTTP/1.1
Pipelining allows multiple requests to be made without waiting for responses
  Server must send responses in same order as received requests
  Reduces application layer latency
GET
200 OK
GET
200 OK
GET
200 OK
TCP open
TCP close

## Slide 11: Network bandwidth
Latency isn’t the only consideration
  There are also limits to the data transfer capacity of the network
  How long will it take to transmit a message?
Content encoding (covered in content negotiation lecture) can be used to compress message bodies
  Smaller message body – less time taken to transmit

## Slide 12: HTTP/2
First major HTTP revision since 1997
  Based in part on earlier SPDY proposal from Google
  Preserves existing HTTP semantics (methods, response codes, headers, etc)
  RFC7540 published 14 May 2015
Offers four improvements over HTTP/1.1:
  Multiplexed requests
  Prioritised requests
  Compressed headers
  Server push
Belshe, M. et al (2015) Hypertext Transfer Protocol Version 2 (HTTP/2). RFC7540. Available at: https://tools.ietf.org/html/rfc7540

## Slide 13: HTTP/2 prioritised requests
A connection may contain multiple streams - multiplexing
  Each stream consists of a sequence of frames
  Each stream has an associated priority
Frames from higher priority streams sent before those from lower priority streams
  Allows asynchronous stream processing (unlike HTTP/1.1 Pipelining)

## Slide 14: HTTP/2 compressed headers
HTTP/1.1 can compress message bodies (using LZW/LZ77/deflate/Brotli)
  Content-Encoding: header (see content negotiation lecture)
  Sends headers in plain text
HTTP/2 also provides the ability to compress message headers

## Slide 15: HTTP/2 server push
HTTP/1.1 servers only send messages in response to requests
HTTP/2 enables a server to pre-emptively send (or push) multiple associated resources to a client in response to a single request.
  Send images, stylesheets, etc before they’re requested by the client

## Slide 16: HTTP/3
Named as future planned development of HTTP in 2018
  Replaces TCP with QUIC over User Datagram Protocol (UDP)
  Addresses shortcoming of HTTP/2; multiplexes are not visible to TCP's loss recovery mechanism, so a lost or reordered packet stalls all active requests
UDP is an unreliable protocol
  No guarantee of delivery or ordering
  Lightweight, however
QUIC
  Eliminates some issues with TCP (blocking if packets are delayed or lost)
  Supports multiplexed connections over UDP
  Designed to reduce TLS overhead (see next lecture)
Bishop, M. (2022) HTTP/3 RFC9114. Available at: https://tools.ietf.org/html/rfc9114

## Slide 17: Further Reading
Fielding, R. and Reschke, J. (2014) Hypertext Transfer Protocol (HTTP/1.1): Message Syntax and Routing. RFC7230. (see §6)
  https://tools.ietf.org/html/rfc7230
Belshe, M. et al (2015) Hypertext Transfer Protocol Version 2 (HTTP/2). RFC7540.
  https://tools.ietf.org/html/rfc7540
Bishop, M. (2020) Hypertext Transport Protocol Version 3 (HTTP/3). Internet Draft.
  https://quicwg.org/base-drafts/draft-ietf-quic-http.html

## Slide 18: Proxies and Caching

## Slide 19: Proxies
Intermediary that acts as server and client
  Receives request from user agent and forwards to origin server
  Returns response to user agent
  Can be chained in sequence
Multiple uses:
  Filtering
  Caching
  Content routing
  Anonymising
  Access control
  Transcoding
Fielding, R. and Reschke, J. (2014) Hypertext Transfer Protocol (HTTP/1.1): Message Syntax and Routing. RFC7230. Available at: https://tools.ietf.org/html/rfc7230
User
Agent
Origin Server
Proxy

## Slide 20: Proxies and HTTP
When sending requests via a proxy, user agent replaces the path in the request line with the full URI
Proxies add Via: headers to all messages they send
  HTTP version, hostname of proxy
  Append to existing header if chaining proxies
GET http://example.org/ HTTP/1.1
Host: example.org
URI to be proxied

## Slide 21
GET http://example.org/ HTTP/1.1
Host: example.org
HTTP/1.1 200 OK
...
GET / HTTP/1.1
Host: example.org Via: HTTP/1.1 proxy.net
HTTP/1.1 200 OK Via: HTTP/1.1 proxy.net
...

## Slide 22: Tunnels
But what about HTTPS?
  TLS guarantees end-to-end encryption of both message body and headers
  Proxies can't understand the request
CONNECT method establishes a tunnel to the destination origin server
  Proxy will forward all subsequent packets in both directions
CONNECT example.org:443 HTTP/1.1
Host: example.org:443

## Slide 23: Proxy Autoconfiguration
proxy.pac file containing sandboxed JavaScript defining FindProxyForURL()
  Configured in browser (specify URI of proxy.pac)
  Configured via DHCP (option 252, containing URI of proxy.pac)
  Configured via DNS (looks for host named wpad, requests wpad.dat)
  Note: common practice, not a (formal) standard
function FindProxyForURL(url, host) { // ... }
Return values:
  DIRECT
  PROXY host:port

## Slide 24: Caching
Recall the following REST constraint: response data must be labelled as cacheable or non-cacheable
In practice, both user agents and proxies may cache representations
  User agent private cache
  Proxy shared cache
How do we know what to cache?
How do we avoid stale data?
Fielding, R. et al (2014) Hypertext Transfer Protocol (HTTP/1.1): Caching. RFC7234. Available at: https://tools.ietf.org/html/rfc7234
User
Agent
Origin Server
Proxy
Cache
Cache

## Slide 25: Key concepts
Freshness/staleness
  How long is it since the representation was generated by the origin server?
  Is there a lifetime (or expiration time) associated with the representation?
Revalidation
  If a cache contains a stale representation, we need to refresh it by either:
    Checking that it is still the same as the representation served by the origin server, or
    Fetching a new (fresh) representation with which to replace it

## Slide 26: Cache headers
Age: seconds
  Sent by a proxy server to indicate how long ago a representation was generated by the origin server
Expires: timestamp
  Indicates when a representation should be considered stale
Cache-Control: directive, directive, ...
  Specifies caching behaviour, may be sent by user agents, proxies and origin servers

## Slide 27: Request Cache-Control: directives
no-cache
  Client will not accept cached representations that have not been validated
no-store
  No part of this request or response may be cached
max-age=seconds
  Client will not accept cached representations more than seconds old
max-stale=seconds
  Client will accept cached representations that are up to seconds past their freshness
min-fresh=seconds
  Client will accept cached representations that will remain fresh for at least seconds
no-transform
  Intermediary must not transform the representation (note: orthogonal to caching)

## Slide 28: Response Cache-Control: directives
no-cache
  Representations may not be reused without being revalidated
no-store
  No part of this request or response may be cached
must-revalidate
  Stale representations may not be reused without being revalidated
max-age=seconds
  Representation is to be considered stale after seconds
public
  Representation may be stored in a shared cache and used for other users
private
  Representation may not be used for other users

## Slide 29
GET http://example.org/ HTTP/1.1
Host: example.org
HTTP/1.1 200 OK Cache-Control: max-age=600
ETag: "39d5-5943f8fdc2607"
GET / HTTP/1.1
Host: example.org
HTTP/1.1 200 OK
Cache-Control: max-age=600 Age: 0
ETag: "39d5-5943f8fdc2607"
http://example.org/
max-age=600, age=0, etag=39d5-5943f8fdc2607

## Slide 30
GET http://example.org/ HTTP/1.1
Host: example.org
HTTP/1.1 200 OK
Cache-Control: max-age=600 ETag: "39d5-5943f8fdc2607" Age: 120
http://example.org/
max-age=600, age=120, etag=39d5-5943f8fdc2607

## Slide 31
GET http://example.org/ HTTP/1.1
Host: example.org
HTTP/1.1 200 OK Cache-Control: max-age=600
ETag: "4b4f-77a6c3ab117a2"
GET / HTTP/1.1
Host: example.org
If-None-Match: "39d5-5943f8fdc2607"
HTTP/1.1 200 OK
Cache-Control: max-age=600 Age: 0
ETag: "4b4f-77a6c3ab117a2"
http://example.org/
max-age=600, age=0, etag=4b4f-77a6c3ab117a2
http://example.org/
max-age=600, age=720, etag=39d5-5943f8fdc2607

## Slide 32
GET http://example.org/ HTTP/1.1
Host: example.org
HTTP/1.1 304 Not Modified Cache-Control: max-age=600
ETag: "39d5-5943f8fdc2607"
GET / HTTP/1.1
Host: example.org
If-None-Match: "39d5-5943f8fdc2607"
HTTP/1.1 200 OK
Cache-Control: max-age=600 Age: 0
ETag: "39d5-5943f8fdc2607"
http://example.org/
max-age=600, age=0, etag=39d5-5943f8fdc2607
http://example.org/
max-age=600, age=720, etag=39d5-5943f8fdc2607

## Slide 33: Caching and content negotiation
We're caching representations, but there may be multiple representations of a given resource
How do when distinguish between the different cached representations of a resource?
Cached representations record the values of the headers listed in the Vary: header
today’s BBC weather forecast for Southampton
Resource
represents
Metadata:
Content-Type: text/html
Data:
<html>
<head>
<title>BBC Weather – Southampton</title>
...
</html>
Representation
represents
Representation
Metadata:
Content-Type: video/mp4
Data:

## Slide 34
GET http://example.org/ HTTP/1.1
Host: example.org
Accept: text/html
HTTP/1.1 200 OK Location: http://example.org/
Content-Type: text/html
Vary: accept, accept-language
GET / HTTP/1.1
Host: example.org
Accept: text/html
HTTP/1.1 200 OK Content-Type: text/html
Vary: accept, accept-language
http://example.org/
max-age=600, age=0, text/html

## Slide 35
GET http://example.org/ HTTP/1.1
Host: example.org
Accept: text/plain
HTTP/1.1 200 OK Content-Type: text/plain
Vary: accept, accept-language
GET / HTTP/1.1
Host: example.org
Accept: text/plain
HTTP/1.1 200 OK Content-Type: text/plain
Vary: accept, accept-language
http://example.org/
max-age=600, age=120, text/html
http://example.org/
max-age=600, age=120, text/html
max-age=600, age=0, text/plain

## Slide 36: Further reading
Fielding, R. and Reschke, J. (2014) Hypertext Transfer Protocol (HTTP/1.1): Message Syntax and Routing. RFC7230.
  https://tools.ietf.org/html/rfc7230
Fielding, R. et al (2014) Hypertext Transfer Protocol (HTTP/1.1): Caching. RFC7234.
  https://tools.ietf.org/html/rfc7234

## Slide 37: Next Lecture: Securing HTTP